## Slide 1: Toward a More Dependable Software Architecture for Autonomous Robots
Matthieu Gallien
DCS Days, Autrans

## Slide 2: Introduction
Can we prove ?
  that a nursebot will not move too quickly for an elderly person leaning on it
  that your service robot is not going to open the gripper and drop the bottle of wine on the floor
  Etc

## Slide 3: Outline
A software architecture for autonomous robots
A component-based language and toolchain
Componentization of the robot software architecture
Verification results
Experimental results

## Slide 4: LAAS Architecture for Autonomous Systems

## Slide 5: One Architecture/Multiple Robots

## Slide 6: Functional Module

## Slide 7: Execution Service
Generic model of an execution service
Based on classic thread life cycle
Executes the application code (codel)
  Code is executed in the states
  The next transition is decided by the executed code

## Slide 8: Design Principle
Easing the development of software for the control of robots
Based on
  Separation of reactive tasks from deliberative tasks:
    Functional/ Decisionnal
  Separation of control and data
  The developer should never think about synchronization primitive
  One function = One module
  The developer should focus on algorithm implementation and not low level details

## Slide 9: GenoM Workflow

## Slide 10: Limitations
No model of the functional layer
  only description of interface
No possibility of static analysis
Centralized controller has limitations (no time, own model, …)
Different representations or models between layers
Needs validation and verification

## Slide 11: Using BIP (Behavior Interaction Priority)
Single model for controller and functional layer
Model that is verifyable and validable
Component-based approach
Allows to specify a distributed controller
Behavior of components can be
  An automata or a Petri-net
  Extended by external C code

## Slide 12: The BIP Framework
Embedded Systems
  Automotive
  Avionics
  Robotics
  Mobile devices
Composition (incremental description)
Layered component model
B E H A V I O R
Interaction Model
(Collaboration)
Priorities
(Conflict resolution)
||
PR2
IM2
PR1
IM1
IM1
PR1
Å
PR2
Å
PR12
IM1
Ä
IM2
Ä
IM12

## Slide 13: BIP: Behavior
An atomic component has
  a set of ports P, for interaction with other comp.
  a set of control states S
  a set of variables V
  a set of transitions of the form :
    p is a port,
    g is a guard, boolean expression on V,
    f is a function on V (block of code)
s1
s2
p, g, f
Notes: POint to the f(x) thing here. as a place holder for your code.

## Slide 14: BIP : Interaction
A connector is a set of ports that can be involved in an interaction
Port attributes (complete, incomplete) are used to distinguish between broadcast and rendezvous

## Slide 15: BIP : Priorities
When 2 interactions are possible, we fire first the one with the highest priority

## Slide 16: Componentization Method
Follow as close as possible the GenoM behavior
Reuse all application code from GenoM
Separate the control from the code execution
Be compatible with the other layer of the architecture
Follow componentization method:
  First identify by top-down approach what are the needed components
  Second identify methods to build a system by combining the atomic components and adding connectors in a bottom-up approach

## Slide 17: How to Decompose this into Components ?
Functional Level::=(Module)+
Module::=(Service)+ . (Execution task)+ . (Poster)+.MsgBox Interface
LAAS Architecture::=Decisional Level.Execution Controller.Functional Level

## Slide 18: GenoM Service
Service::=Controller.Activity

## Slide 19: BIP Model: Execution Task
Execution Task::=Timer.Scheduler

## Slide 20: How to build a Functional Level
Module
Module
Module
Module
Module
Functional Level

## Slide 21: Semi-Automatic Translation from GenoM to BIP
Generate BIP models from GenoM module descriptions
Generate C code needed to implement legacy interfaces to the module
  Allow for seamless integration in the LAAS architecture
Needs manual modification of the C code libraries in order to have all synchronizations in the BIP model

## Slide 22: Summary of Implementation
Works with the distributed BIP engine
  GenoM generates one process for each module
  Necessary to rely on the operating system to do fine grained interleaving
Simulate clocks with sleep (i.e. call to the operating system)

## Slide 23: GenoM - BIP Toolchain
BIP
Codels
+
V&V
D-Finder
Aldebaran
etc
BIP Models
BIP
Controller
BIP
Controller
BIP
Controller
GenoM
Models
+
module Motion {
number: 9600;
SDI: MOTION_DATA;
}
request SetPos {
type: control;
input: pos::pos;
control: controlPos;
report: BAD_PARAM;
}
task Move {
period: 25;
priority: 15;
}

## Slide 24: D-Finder
Can analyse BIP models without computing the reachable states;
Uses invariants to approximate the reachable states
Used to verify properties like the deadlock freedom on BIP models of the LAAS architecture
  Deadlock freedom of the NDD module: 3 hours to detect the lack of deadlock
  Discovered problems in the models that could cause deadlocks during execution

## Slide 25: Encoding Constraints in the BIP model
One example: Data freshness
  If a service needs data, it needs up-to-date data
  GenoM translates this into « Poster reads »
  Adding constraints into the BIP model to forbid reading an outdated poster

## Slide 26: Experimental Results
Functional layer of Dala Robot is 8 modules
  Complete navigation loop (4 modules) is modeled and generated with BIP
  4 modules are still generated with GenoM
  Except the functional layer, nothing change
Test with the real robot and a simulator
Test in normal condition and also with faults

## Slide 27: Experimental Results
3 videos
  Demonstrate normal behavior with BIP
  Demonstrate that GenoM by itself cannot avoid faults or can contain bugs
  Demonstrate that the controller resulting of the constraints and the BIP execution engine is safer

## Slide 28: Normal Run with BIP

## Slide 29: Faulty Run with GenoM

## Slide 30: Fault Avoided with BIP

## Slide 31: Conclusion
Development of a methodology to componentize the Functional Level of the LAAS Architecture
Development of a tool that produces BIP models from GenoM modules
Preliminary results about the verification and validation of the BIP models
Preliminary results about adding desired constraints into the BIP model

## Slide 32: BIP Model: Full module

## Slide 33: BIP models
MsgBox Interface
Control
Service
MsgBox Interface::=Timer.MsgBox Client

## Slide 34: BIP Models
Poster
SDI Lock
Timer

## Slide 35: Atomic Components
Timer
SDI lock
Poster
Control Service
Execution Service Controller
Execution Service Activity
Scheduler