## Slide 1: DOL-Critical/BIP Tool Chain Demo
ETH Zurich, UJF Verimag

## Slide 2: DOL-Critical/BIP Tool Chain
OFFLINE
ONLINE
Optimize task mapping and TTS schedule
Verify functional correctness and timing properties
Execute the FMS application on MPPA

## Slide 3: System Specification
Specification
Preprocessing
Offline Opt.
DOLC  BIP Translation
Functional Simulation
app.xml/arch.xml
app.xml/arch.xml
mapping.xml
DOL-C code /
TTS Schedule
Application
  XML specification
    Tasks & Controllers
    Data channels for inter-task comm.
    Control channels for task-controller comm.
  DOL-C code
    Task functionality
Architecture
  Hierarchical representation of
  multi-core platform

## Slide 4: Application
Specification
Preprocessing
Offline Opt.
DOLC  BIP Translation
Functional Simulation
app.xml/arch.xml
app.xml/arch.xml
mapping.xml
Wrapper threads/ TTS Scheduler
Application inspired by Sensors task
sub-group of the FMS
  6 periodic tasks
  4 mailboxes, 1 blackboard
Writes its activation number to the mailbox
Writes the number of data read from the mailboxes to the blackboard
Reads the data from the blackboard

## Slide 5: Architecture
Specification
Preprocessing
Offline Opt.
DOLC  BIP Translation
Functional Simulation
app.xml/arch.xml
app.xml/arch.xml
mapping.xml
Wrapper threads/ TTS Scheduler
Single computational cluster
  16 cores with shared memory
  Connected by a local bus
Core 0
Core 1
Core 15
…
Memory

## Slide 6: Step 1: Preprocessing
Offline Opt.
DOLC  BIP Translation
Functional Simulation
app.xml/arch.xml
app.xml/arch.xml
mapping.xml
Wrapper threads/ TTS Scheduler
Validation of the XML files
  Application
  Architecture
Consistency checks
Extraction of data required for
mapping & scheduling optimization
Preprocessing
Specification

## Slide 7: Step 2: Mapping & TTS Schedule Optimization
Simulated Annealing
DOLC  BIP Translation
Functional Simulation
app.xml/arch.xml
app.xml/arch.xml
mapping.xml
Wrapper threads/ TTS Scheduler
Specification
Preprocessing
Offline Opt.
MCMSO
mapping generation and variation
candidate mapping
Interference analysis
Objectives:
  Maximize aggregate slack time at the
  end of the frames
  Minimize number of cores

## Slide 8: Step 2: Mapping & TTS Schedule Optimization
Simulated Annealing
DOLC  BIP Translation
Functional Simulation
app.xml/arch.xml
app.xml/arch.xml
mapping.xml
Wrapper threads/ TTS Scheduler
Specification
Preprocessing
Offline Opt.
MCMSO
mapping generation and variation
candidate mapping
Interference analysis

## Slide 9: Step 3: DOL-Critical to BIP
Functional Simulation
app.xml/arch.xml
app.xml/arch.xml
app.xml;mapping.xml
APP+TTS Scheduler
BIP Models
Specification
Preprocessing
Offline Opt.
DOLC  BIP Translation
TTS Cycle BIP component cycle length 200ms
TTS Frame f1
TTS Frame f1
TTS Frame f3
TTS Frame f3
f1 A
f1 B
f2 A
f2 B
f3 A
f3 B
f4 A
f4 B
p5
BB
p6
mb
mb
mb
mb
p1
p2
p3
p4

## Slide 10: Step 4: Functional Simulation
app.xml/arch.xml
app.xml/arch.xml
Specification
Preprocessing
Offline Opt.
DOLC  BIP Translation
Functional Simulation
app.xml;mapping.xml
APP+TTS Scheduler
BIP Models
10
28/02/2014
TTS Cycle BIP component cycle length 200ms
TTS Frame f1
TTS Frame f1
TTS Frame f3
TTS Frame f3
f1 A
f1 B
f1 A
f1 B
f1 A
f1 B
f1 A
f1 B
p5
BB
p6
mb
mb
mb
mb
p1
p2
p3
p4
BIP Components  C++ classes
BIP Engine Class
Trigger component execution according to BIP semantics
TTS Cycle